## Slide 1: KI23400 / KI27400 Series Loss Test Meter Training Manual Revision: 8 Date: 14 Oct 2024

## Slide 2: Table of Content (TOC)
General Features (Slide 3)
Instrument Overview & Layout (Slide 4)
Getting Started
➥ Select test cord configuration (Slide 5)
➥ Install / uninstall connector adaptor (Slide 6)
➥ Power ➥ External via USB (Slide 7)
➥ Batteries (Slide 8)
➥ Disable / enable battery charging (Slide 9)
➥ On / off instrument & LCD-backlight (Slide 10)
➥ To view firmware version & instrument serial number (Slide 11)
➥ To show all display segments of LCD (Slide 12)
Instrument Operation ➥ 2-way Autotest operation (Slides 13~20)
➥ 1-way Autotest operation (Slides 21~28)
➥ Restricted wavelength Autotest operation (Slides 29~31)
➥ Autotest User-to-User Communication operation (Slides 32~33)
➥ Light source manual operation (Slides 34~37)
➥ Power meter manual operation (Slides 38~46)
➥ ORL Meter (optional) manual operation (Slides 47)
➥ Tone detection operation (Slide 48)
➥ Slow Mode operation (Slide 49)
➥ Memory operation ➥ Store data into internal memory (Slide 50)
➥ Recall stored data from internal memory (Slides 51~58)
➥ Retest or overwrite results (Slides 59~60)
➥ Transfer internally stored data onto USB stick (Slide 62)
➥ Clear internal memory (Slide 63)
➥ Instrument Data Sanitization (Slide 64)
➥ Text ID Tag operation (Slides 65~70)
➥ Visible laser operation (Slide 71)
Instrument Settings ➥ Date & time (Slide 72)
➥ To deactivate beeping (Slide 73)
➥ To activate Slow Mode at instrument switch-on (Slide 74)
➥ Pass / fail thresholds setting (Slides 75~77)
➥ ORL UCAL (User CALibration) setting (Slides 78~79)
➥ ORL Zero Function (Slides 80~81)
➥ Reset ORL UCAL & NF (for Zero Function) to factory defaults (Slides 82)

## Slide 3: General Features
Return to TOC
Ease to use, slim & versatile
1-hookup bidirectional test (SM + MM) for Loss, length*, ORL*
Real time auto pass / fail
Larger, sunlight readable & backlit LCD
SM, MM (EF Compliant) & quad test options
Large memory & USB key file dump
Interchangeable connectors
Real-time, secure PC reporting software
* Only available on selected model
Continuity test tone with Multi-Fiber ID
VFL VisiTester* option
Long battery life, USB external power
>25 calibration λ, 1% accuracy
ISO 17025 traceable calibration
3 Year warranty & calibration cycle
Made in Australia

## Slide 4: Instrument Overview & Layout
On/Off
LCD Backlight
Micro-USB of USB-C (for newer instrument version) port for external power
& computer interface
Connector Cover
Lanyard holder
LCD
Keypad
Connector release
(SM 2-way port)
Connector release
(Power Meter port)
Connector release
(MM 2-way port)
Store/transfer memory
Battery door
Anti-slippery pad
USB port for memory stick
Product label
Instrument model
Option included:
ORL, Leng (Length), Visi (VisiTester)
Return to TOC

## Slide 5: Getting Started ➥ Select test cord configuration
Identify fibre type required for test cord and configuration required. Instrument supplied with SC connector adaptor as standard.
Standard connector types:
XL connector types:
Note: Unlike light sources, power meters accept both PC and APC connectors.
SC/SC-hybrid connector adaptor
Return to TOC

## Slide 6: Getting Started ➥ Install / uninstall connector adaptor
❶ Press down release button with finger of one hand.
❷ Pull out existing adaptor with the other hand.
❸ Push in a new adaptor.
❷
❸
Adaptor slot on this side
❶
Return to TOC
SM 2-way port
MM 2-way port
Power Meter port
The instrument comes with 2 or 3 ports (i.e., 1x or 2x 2-way port/s and 1x Power Meter port) depending on the models. See picture on the right for locations of these ports.
Install and uninstall connector adaptors to these ports as per steps below:

## Slide 7: Getting Started ➥ Power ➥ External via USB
USB-A (to computer or power pack)
Caution: When external source is connected, batteries in instrument will be charged if recharging is enabled.
To avoid recharging non-rechargeable batteries which may lead to acid leakage and instrument damage, make sure that recharging is disabled whenever these batteries are used.
See section, Disable/enable battery charging.
Connect instrument to a computer or an external power pack via the micro-USB or USB-C (for newer instrument version) connector marked “DC-PWR-IN”.
Micro-USB or USB-C
Return to TOC

## Slide 8: Getting Started ➥ Power ➥ Batteries
Caution: Battery charging on instrument must first be disabled when using non-rechargeable batteries. See next page for instructions to disable battery charging.
Note:
Instrument’s date / time setting holds for approx. 2 minutes during batteries change over.
Use 2x Alkaline / Lithium AA cells or 2 x NiMH AA cells.
Alkaline battery run time up to approx. 1,000 hours.
To install / uninstall batteries:
➀ Unclip door of battery compartment at rear of instrument.
➁ Insert / remove batteries. Make sure that batteries are inserted in the correct polarities.
Battery compartment
Return to TOC

## Slide 9: Getting Started ➥ Disable / enable battery charging
Insert the supplied programming-shunt across the pins inside battery compartment to disable or enable charging as shown below.
Note: Instrument comes with the shut in this position.
Battery charging enabled:
Supplied 0.1” pitch programming-shunt
Supplied 0.1” pitch programming-shunt
OR
Battery charging disabled:
programming-shunt is removed
Programming pins inside battery compartment
Return to TOC

## Slide 10: Getting Started ➥ On / off instrument & LCD-backlight
Battery charge indicator
“Month, Day”, “Time”, “Year”
(Upon powering up, instrument may require these to be entered e.g. after batteries are replaced.
Auto off feature:
When powered with batteries, instrument will switch off automatically 10 minutes after the last keypress.
To disable auto power off, press and hold green button for 3 seconds or until beeping stops. ‘Perm’ will display on the upper LHS of the LCD.
When powered via USB, auto off feature is automatically disabled.
To switch on:
Press the green button.
To switch off:
Press the green again.
LCD backlight: Press button below the light bulb symbol to turn backlight on or off.
Home display (Main menu)
Return to TOC

## Slide 11: Getting Started ➥ To view firmware version & instrument serial number
➀ When instrument is off, hold down F4 then press green button.
Instrument serial number
Firmware version
Home display is shown after button is released.
➁ Continue to hold down F4.
➂ Release F4.
HOLD
HOLD
Return to TOC
Hardware version

## Slide 12: Getting Started ➥ To show all display segments of LCD
➀ When instrument is off, hold down F1 then press green button.
Full segment display
Home display is shown after buttons are released.
➁ Continue to hold down F1.
➂ Release F1.
HOLD
HOLD
Return to TOC

## Slide 13: Instrument Operation ➥ 2-way Autotest operation
Work with a pair of instruments (same model) only
Performs bidirectional loss, ORL (optional), cable length (optional) measurements
Displays test result (pass/fail) automatically
➀ Connect the 2-way ports of both instruments with a reference patch-lead.
IMPORTANT:
Light (especially fluorescent) entering the instruments via Power Meter ports may result in Autotest malfunctioning, so cover these ports on both instruments with opaque dust caps.
SM
2-way port
MM
2-way port
➁ Start Autotest:
Press F4 on any of the instruments.
Continue next page
Reference patch-lead
Return to TOC
Adaptor on Power Meter Port covered with an opaque dust cap
Adaptor on Power Meter Port covered with an opaque dust cap

## Slide 14: Instrument Operation ➥ 2-way Autotest operation (continue)
➂ Set reference: On any instrument, press down F2 until beeping stops.
Continue next page
Reference patch-lead
Indicating instrument operating in 2-way Autotest mode
Flash to indicatesunit is operating in Autotest mode
Test data (bidirectional losses & their respective averages) and results,
for all active wavelengths are displayed here.
for each wavelength are shown in a row.
3 wavelengths can be shown simultaneously at a time. If more than 3 active wavelengths, screen auto scrolls & cycles to show all wavelengths
Arrow sign indicating the data row which is being updated.
When Autotest starts, LCD of both instruments display losses of each direction and their respective averages for all active wavelengths.
For restricted wavelength Autotest, refer to slides 29~31.
“Test Summary” display
“Test Summary” display
Return to TOC

## Slide 15: Instrument Operation ➥ 2-way Autotest operation (continue)
➃ Reconnect instruments’ ports with DUT (Device Under Test) fiber.
Continue next page
Reference patch-lead
When “SET REF” & “bUSY” stop blinking, values for cable length (optional), losses & average losses displayed on both instruments are zeroed momentarily.
“Test Summary” display
“Test Summary” display
Return to TOC
Note:
The master unit (where Autotest was initiated) will be in Autotest standby mode if the fiber is disconnected from the 2-way ports for long enough. Autotest will resume automatically when a fiber is reconnected.
Allow approx. 10 seconds for the instruments’ displays to be updated with test data for a newly connected fiber.

## Slide 16: Instrument Operation ➥ 2-way Autotest operation (continue)
Continue next page
DUT fiber
Location-A
Location-B
〰
〰
〰
〰
Cable length measured on Unit A:
Flashes (fail) if measured value is greater than set threshold.
Average loss (dB) of B►A & A►B @ 1310 nm
A►B loss (dBm) @ 1310 nm
B►A loss (dBm) @ 1310 nm
Average loss (dB) of A►B & B►A @ 1310 nm
B►A loss (dBm) @ 1310 nm
A►B loss (dBm) @ 1310 nm
Symbol signifying loss & ORLs(optional) pass/fail against the set thresholds (refer to Pass/fail Threshold Setting, slides 75~77) for a wavelength:
If AV (Average) method is selected:
“✓” : Pass/fail check is disabled (threshold value is set at “0”).
or
“✓” (pass): Average loss value (magnitude) is smaller than or equals to PASS threshold and, ORL (optional) passes.
Flashing “X” (marginal): Average loss value (magnitude) is greater than PASS but, smaller than or equals to MARGINAL thresholds and, ORL (optional) passes.
“X” (fail): Average loss value (magnitude) is greater than MARGINAL thresholds or, ORL (optional) fails.
If WC (Worst Case) method is selected:
“✓”: Pass/fail check is disabled (threshold value is set as “0”).
“✓” (pass): Worst case loss value (magnitude) is smaller than or equals to PASS threshold and, ORL (optional) passes.
Flashing “X” (marginal): Worst case loss value (magnitude) is greater than PASS but, smaller than or equals to MARGINAL thresholds and, ORL (optional) passes.
“X” (fail): Worst case loss value (magnitude) is greater than MARGINAL threshold or, ORL (optional) fails.
Note: For consistent pass/fail results, ensure the same thresholds are set on both instruments.
Overall test result (“PASS” / “FAIL”):
“PASS”: if test result for loss of all wavelengths are “✓” or marginal (blinking “X”) and,, cable length (optional) test passes and, ORL (optional) test passes.
“FAIL”: if loss or ORL (optional) test result of any wavelength is “X” or, length (optional) test fails (blinking).
Note: For accurate pass/fail result on instrument model without Length and ORL options, set all thresholds for ORL and length to “0” (disabling them).
“Test Summary” display
“Test Summary” display
Return to TOC
➄ Display “Test Detail”: press F3 on one of the instruments.
Cable length measured on Unit B:
Flashes (fail) if measured value is greater than set threshold.

## Slide 17: Instrument Operation ➥ 2-way Autotest operation (continue)
Continue next page
DUT fiber
Location-A
Location-B
A►B absolute power @ 1310 nm.
“Test Summary” display
“Test Detail” display
Symbol signifying loss pass/fail against set threshold for a wavelength:
“✓” - Pass/fail check is disabled (threshold value is set as “0”).
or
“✓” (pass) - Loss values (magnitude) for both directions are smaller than or equal to PASS threshold.
Flashing “X” (marginal) - Loss value (magnitude) for either or both direction/s is/are greater than PASS but smaller than or equal to MARGINAL thresholds.
“X” (fail) - Loss value (magnitude) for one or both direction/s is/are greater than MARGINAL threshold.
At this display, press ‘+’ or ‘-” button to show loss data/result of other active wavelengths.
Return to TOC
〰
〰
〰
〰
A►B loss @ 1310 nm.
A►B stored reference power @ 1310 nm.
B►A absolute power, loss, reference power @ 1310 nm.
km

## Slide 18: Instrument Operation ➥ 2-way Autotest operation (continue)
〰
〰
Continue next pages,
to display ORL (optional) measurements & test result
To stop 2-way Autotest
DUT fiber
Location-A
Location-B
Nominal power of Sources
“Test Summary” display
“Test Detail” display
Return to TOC
HOLD
➅ Display Source’s nominal power:
Hold down Toggle Centre.
LCD will return to previous display after button is released.
km
〰
〰

## Slide 19: Instrument Operation ➥ 2-way Autotest operation (continue)
〰
〰
DUT fiber
Location-A
Location-B
“Test Summary” display
“Test Detail” display
Return to TOC
➆ Enter ORL Test display:
Press F3.
km
〰
〰
〰
〰
DUT fiber
Location-A
Location-B
“Test Summary” display
“ORL Test” display
〰
〰
A►B ORL value @ 1310 nm
B►A ORL value @ 1310 nm
UCAL offset value for 1310 nm (see ORL UCAL Setting section)
Symbol signifying ORL pass/fail against set thresholds for a wavelength:
“✓” - Pass/fail check is disabled (threshold is set at “0.00”.
or
“✓” (pass) - ORL values (magnitude) for both directions are larger or equal to the set thresholds.
“X” (fail) - ORL value/s (magnitude) for one or both direction/s is/are smaller than the set thresholds.
On this display,
press ‘+’ or ‘-” button to show ORL data/result of other active wavelengths.
Press F3 continuously to toggle between ORL Test, Test Summary, Test Detail displays.
Continue next page
*NOTE:
For accurate ORL measurement on instruments with two 2-way ports, insert PC or APC Terminators as appropriate onto the unused ports to prevent stray light from entering the instrument.
*
*

## Slide 20: Instrument Operation ➥ 2-way Autotest operation (continue)
〰
〰
DUT fiber
Location-A
Location-B
Flashing indicates display stops updating.
Press F4 again resume display update.
“Test Summary” display
“ORL Test” display
➈ Stop Autotest: Press down F1 until a beep is heard on any of the instruments.
Return to TOC
➇ Stop/resume display update:
Press F4 repeatedly.
〰
〰
➈

## Slide 21: Instrument Operation ➥ 1-way Autotest operation
Performs 1-direction loss. Work with a single instrument or a pair of instruments.
➀ Connect ports on the same instrument with a reference patch-lead as shown below.
➀ Connect ports of the 2 instruments with a reference patch-lead as shown below.
➁ Start Autotest: press F4.
UNIT #1 (Source)
UNIT #2 (Meter)
SM
2-way port
Meter port
MM
2-way port
Meter port
Continue next page
Continue next page
Single Instrument
A pair of Instruments
Home display
SM
2-way port
MM
2-way port
Home display
Home display
➁ Start Autotest (on Source-unit): press F4.
Return to TOC
Reference patch-lead
Reference patch-lead

## Slide 22: Instrument Operation ➥ 1-way Autotest operation (continue)
➂ Set reference: Press F2 on meter-unit until beeping stops.
Indicating 1-way Autotest mode
Flashing “AUTO” indicating unit operating in Autotest mode
Test data and results,
for all the wavelengths received from source are displayed here.
for each wavelength are shown in a row.
for 3 wavelengths can be shown simultaneously at a time. If more than 3 wavelengths, screen will scrow and cycle to show all.
Arrow indicating data row which is being updated.
Continue next page
Single Instrument
A pair of Instruments
Continue next page
Cycle to display all active wavelengths
➂ Set reference: Press F2 on meter-unit until beeping stops.
Return to TOC
Reference patch-lead
Reference patch-lead
PASS
PASS

## Slide 23: Instrument Operation ➥ 1-way Autotest operation (continue)
Continue next page
Single Instrument
A pair of Instruments
Continue next page
Loss value is zeroed momentarily.
Stored reference value is displayed here.
Return to TOC
Reference patch-lead
Reference patch-lead
➃ Reconnect ports with DUT fiber cable.
➃ Reconnect ports with DUT fiber cable.
PASS
PASS
When “SET REF” & “bUSY” stop blinking:

## Slide 24: Instrument Operation ➥ 1-way Autotest operation (continue)
〰
〰
〰
〰
〰
〰
〰
〰
Symbol signifying loss pass/fail against the set thresholds (refer Pass/fail Threshold Setting section) for each wavelength:
“✓” : Pass/fail check is disabled (threshold value is set as “0”).
or
“✓” (pass): loss value (magnitude) smaller than or equals to PASS threshold.
Flashing “X” (marginal): loss value (magnitude) greater than PASS threshold but smaller than or equals to MARGINAL threshold.
“X” (fail): loss value (magnitude) greater than MARGINAL threshold.
Absolute power (dBm)
Continue next page
Loss in dB
Reference power in dBm
➄ Display absolute power in watt: Press F3 on meter-unit.
PASS
FAIL
Overall test result:
“PASS”: if test results for all wavelengths are “✓” or marginal (blinking “X”.)
“FAIL”: if test result of 1 or more wavelength fails.
Single Instrument
A pair of Instruments
Continue next page
➄ Display absolute power in watt: Press F3 on meter-unit.
FAIL
PASS
Return to TOC
DUT fiber
DUT fiber

## Slide 25: Instrument Operation ➥ 1-way Autotest operation (continue)
〰
〰
〰
〰
Absolute power in Watt
Continue next page
PASS
➅ Return display to show absolute power in dBm & loss in dB: Press F3 again.
Single Instrument
A pair of Instruments
Continue next page
〰
〰
〰
〰
Return to TOC
➅ Return display to show absolute power in dBm & loss in dB: Press F3 again.
DUT fiber
DUT fiber

## Slide 26: Instrument Operation ➥ 1-way Autotest operation (continue)
〰
〰
〰
〰
〰
〰
〰
〰
Loss in dB
Continue next page
PASS
Single Instrument
A pair of Instruments
Continue next page
Absolute power in dBm
PASS
FAIL
Return to TOC
DUT fiber
DUT fiber

## Slide 27: Instrument Operation ➥ 1-way Autotest operation (continue)
〰
〰
〰
〰
〰
〰
〰
〰
Continue next page
Single Instrument
A pair of Instruments
Continue next page
Source nominal power
Return to TOC
➆ Display Source’s nominal power: Hold down Toggle Centre.
➆ Display Source’s nominal power: Hold down Toggle Centre.
HOLD
HOLD
DUT fiber
DUT fiber
PASS
PASS

## Slide 28: Instrument Operation ➥ 1-way Autotest operation (continue)
〰
〰
〰
〰
〰
〰
〰
〰
PASS
Single Instrument
A pair of Instruments
➈ Stop Autotest: Press F1.
Flashing “HOLD” indicates update has stopped.
PASS
Return to TOC
➇ Stop / resume display update: Press F4 repeatedly.
DUT fiber
DUT fiber
Note:
After the next fiber is connected during DUT change-over (without stopping Autotest), allow approx. 10 seconds for the instruments’ displays to be updated with data for that newly connected fiber.
➇ Stop / resume display update: Press F4 repeatedly.
➈ Stop Autotest: Press F1 on Source-unit or disconnect the fiber for more than 8 seconds.

## Slide 29: Instrument Operation ➥ Restricted wavelength Autotest operation
There are two different ways (Method 1 & Method 2) to restrict the number of active λ for Autotest.
Method 1 (only applicable to instrument with 2x 2-way ports) :
a. To start λ-restricted Autotest: for SM port only (e.g., 1310-1550 nm on a Quad instrument):
At Home display, press ‘-’and F4 simultaneously.
b. To start λ-restricted Autotest: for MM port only (e.g., 850-1300 nm on a Quad-instrument) :
At Home display, press ‘+’ and F4 simultaneously.
SM
2-way port
MM,
2-way port
Return to TOC

## Slide 30: Instrument Operation ➥ Restricted-wavelength Autotest operation (continue)
Method 2:
➀ Excluding (deactivating) wavelength for Autotest:
➊ At Source mode, select the wavelength to be excluded/deactivated for Autotest e.g., 1550 nm: press ‘+’or ‘-”.
➋ View status of selected wavelength: hold down F4.
➌ “Deactivate” the selected wavelength: continue to hold down F4 then press Toggle Centre.
HOLD
HOLD
HOLD
➍ Release F4.
Continue next page
1550 nm has been selected.
“in” indicating 1550 nm is currently activated (included for Autotest).
“Out” indicating 1550 nm is “deactivated” (excluded for Autotest).
Return to TOC
UNIT #1
UNIT #1
UNIT #1
UNIT #1

## Slide 31: Instrument Operation ➥ Restricted-wavelength Autotest operation (continue)
Method 2 (continue):
➁ Start restricted-λ Autotest (with the selected wavelength excluded)
➏ Start restricted-wavelength Autotest: press Toggle Centre and F4 simultaneously, on the unit which wavelength deactivation was performed.
➎ Exit Source mode: press F1 Note: press Toggle Center to turn off Source prior to exiting.
E.g., If the Source-instrument is a 2 wavelengths models with 1310-1550 nm sources, only “1310” displays here indicating that Autotest is running in restricted mode with only 1310 nm.
〰
〰
〰
〰
E.g., In a 1-way Autotest operation, only test data and result for 1310 nm will be displayed. on Meter-instrument.
Return to TOC
UNIT #1
UNIT #1
UNIT #1
UNIT #2

## Slide 32: Instrument Operation ➥ Autotest user-to-user communication operation
Apply to 2-way Autotest only.
Near-end Instrument
Far-end Instrument
➀ Near-end unit to signal Far-end unit during 2-way Autotest:
Near-end Instrument
Far-end Instrument
“HOLD” flashing & display update stops.
Unit beeps once and, “HOLD” flashing & display update stops.
Press F4
Return to TOC

## Slide 33: Instrument Operation ➥ Autotest user-to-user communication operation (continue)
Near-end Instrument
Far-end Instrument
② Far-end unit to respond to Near-end unit during 2-way Autotest :
Near-end Instrument
Far-end Instrument
“HOLD” stops flashing & display update resumes.
Unit beeps once and, “HOLD” stops flashing & display update resume.
Press F4
Return to TOC

## Slide 34: Instrument Operation ➥ Light source manual operation
Enter Source mode:
At Main menu (Home display), press F1.
a. Select wavelength or on/off output:
Available functions:
a. Select wavelength or on/off output
b. Adjust output power of selected wavelength
c. Select between CW (Continuous Wave) or Tone (modulation) output mode
d. Exit Source mode
➊ Press ‘+’ or ‘-’ to cycle through & select an operating wavelength or, turn the output on/off off .
➋ Press Toggle Centre will turn output on or off.
Continue next page
CW mode
Return to TOC

## Slide 35: Instrument Operation ➥ Light source manual operation (continue)
b. Adjust output power of the selected wavelength:
- for laser source only
- output power can be adjusted in 0.01 dB steps for 7 dB.
➊ To adjust power level: hold down F2, then press ‘+’ or ‘-’.
Holding down ‘+’ or ‘-’ to speed up incremental or decremental of power levels.
➋ To toggle to max and min power levels: hold down F2 then, press Toggle Centre repeatedly.
Continue next page
HOLD
Max power level
Min power level
HOLD
HOLD
Return to TOC

## Slide 36: Instrument Operation ➥ Light source manual operation (continue)
C. Select between CW (Continuous Wave) or Tone (modulation) output mode:
Available test tones/id tones selectable in this sequence: On (CW), 270 Hz, 1000 Hz, 2000 Hz, id1 (300 Hz), id2 (400 Hz), id3 (500 Hz), id4 (600 Hz), id5 (700 Hz), id6 (800 Hz), id7 (900 Hz), id8 (1100 Hz), id9 (1200 Hz), id10 (1300 Hz), id11 (1400 Hz), id12 (1500 Hz).
To start test/Id tone mode:
At CW output mode, press F3 repeatedly to scroll through & select one from the available test/id tones.
Alternatively, hold down F3 and then press ‘+’ or ‘-’.
To end tone (modulation) output mode:
Hold down F3 for 3 seconds.
Alternatively, hold down F3 then, press Toggle Centre.
Continue next page
HOLD
HOLD
HOLD
CW output mode
“Hz”
CW output mode
Tone output mode
Return to TOC

## Slide 37: Instrument Operation ➥ Light source manual operation (continue)
d. Exit Source mode:
Press F1 to exit Source mode & return to Home display (Main menu).
Note:
If the output is not turn off prior to exiting Source Mode, it will remain ‘on’.
To ensure that output is off after exiting Source mode, turn off output as per the instructions on slide 34, before F1 is pressed.
Return to TOC

## Slide 38: Instrument Operation ➥ Power meter manual operation
Measure power with a single instrument or a pair of instruments
➀ Connect ports on the same instrument with a reference patch-lead &,
select Source to output at CW mode at a wavelength (refer to Light Source Manual Operation section.)
➀ Connect ports of 2 instruments &,
select source-instrument to output at CW mode at a wavelength (refer to Light Source Manual Operation section.)
➁ Exit Source: mode: press F1.
UNIT #1 (Source)
UNIT #2 (Meter)
SM
2-way port
Meter port
MM
2-way port
Meter port
Continue next page
Continue next page
Single Instrument
A pair of Instruments
Home display
Home display
Source mode display
Source mode display
➂ Enter Meter mode: press F3.
➁ Enter Meter mode:
Press F3
SM
2-way port
MM
2-way port
E.g. 1550 nm is selected for output.
Return to TOC
Reference patch-lead
Reference patch-lead
Reference patch-lead

## Slide 39: Instrument Operation ➥ Power meter manual operation (continue)
➃ Select the matching λ of source: press ‘+’ or ‘-’.
UNIT #1 (Source)
UNIT #2 (Meter)
Continue next page
Continue next page
Wavelength (nm)
Absolute power (dBm)
Loss (dB)
Reference power (dB)
➂ Select λ ( same as that on source): press ‘+’ or ‘-’.
Meter mode display
Text ID Tag (refer to Test ID Tag Operation Slides (61~66).
Single Instrument
A pair of Instruments
Return to TOC
Reference patch-lead
Reference patch-lead

## Slide 40: Instrument Operation ➥ Power meter manual operation (continue)
➄ Set reference: press and hold F2 until beeping stops.
UNIT #1 (Source)
UNIT #2 (Meter)
Continue next page
Continue next page
Meter mode display
E.g.: Wavelength 1550 nm is selected to math that of the Source.
➃ Set reference: press and hold F2 until beeping stops.
Single Instrument
A pair of Instruments
Return to TOC
Reference patch-lead
Reference patch-lead

## Slide 41: Instrument Operation ➥ Power meter manual operation (continue)
➅ Display absolute power in watt:
press F3.
UNIT #1 (Source)
UNIT #2 (Meter)
Continue next page
Continue next page
Loss value is zeroed.
Stored reference value displayed here.
➄ Display absolute power in watt:
press F3.
Single Instrument
A pair of Instruments
Return to TOC
Reference patch-lead
Reference patch-lead

## Slide 42: Instrument Operation ➥ Power meter manual operation (continue)
〰
〰
〰
〰
UNIT #1 (Source)
UNIT #2 (Meter)
Continue next page
Continue next page
➆ Display min and max absolute power values in watt: press ‘+’ & ‘-’ simultaneously.
Absolute power (dBm).
Absolute power (Watt).
➅ Display min and max absolute power values in watt: press ‘+’ & ‘-’ simultaneously.
〰
〰
〰
〰
Single Instrument
A pair of Instruments
Return to TOC
DUT fiber
DUT fiber

## Slide 43: Instrument Operation ➥ Power meter manual operation (continue)
〰
〰
〰
〰
UNIT #1 (Source)
UNIT #2 (Meter)
Continue next page
Continue next page
➇ Display min and max absolute power & loss values in dBm & dB: press F3.
Max absolute power in dBm & watt respectively
Min absolute power in dBm & watt respectively
➆ Display min and max absolute power & loss values in dBm & dB: press F3.
〰
〰
〰
〰
Single Instrument
A pair of Instruments
Return to TOC
DUT fiberd
DUT fiber

## Slide 44: Instrument Operation ➥ Power meter manual operation (continue)
〰
〰
〰
〰
〰
〰
〰
〰
〰
〰
〰
〰
UNIT #1 (Source)
UNIT #2 (Meter)
Continue next page
Continue next page
➈ To exit max/min values display:
Press ’+’ & ‘-’ simultaneously again.
Max absolute power in dBm & watt respectively
Min absolute power in dBm & watt respectively
➇ To exit max/min values display:
Press ’+’ & ‘-’ simultaneously again.
Single Instrument
A pair of Instruments
Return to TOC
DUT fiber
DUT fiber

## Slide 45: Instrument Operation ➥ Power meter manual operation (continue)
〰
〰
〰
〰
UNIT #1 (Source)
UNIT #2 (Meter)
Continue next page
Continue next page
➉ To stop / resume display update:
press F4 repeatedly.
➈ To stop / start display update:
press F4.
〰
〰
〰
〰
Single Instrument
A pair of Instruments
Return to TOC
DUT patch-lead
DUT patch-lead

## Slide 46: Instrument Operation ➥ Power meter manual operation (continue)
〰
〰
〰
〰
UNIT #1 (Source)
UNIT #2 (Meter)
“ HOLD” flashes indicating display update stops.
To resume display update, press F4 again.
⑪ To exit Meter mode: Press F1
(LCD will return to Home display).
➉ To exit Meter mode: Press F1
(LCD will return to Home display).
〰
〰
〰
〰
Single Instrument
A pair of Instruments
Return to TOC
DUT fiber
DUT fiber

## Slide 47: Instrument Operation ➥ ORL Meter (optional) manual operation
➂ Exit ORL measurement mode:
Press F1 to return to Home Display.
Return to TOC
➀ Enter ORL measurement mode:
At Home Display , press F2
➁ Connect DUT onto the appropriate 2-way port
Measured ORL (dB) of DUT @ 1310 nm.
Press “+”or “-” to view ORL values of other active wavelengths.
UCAL offset (refer to slides 78, 79)
Home display
Home display
ORL mode display
ORL mode display
DUT
SM
port
MM
port
DUT
* NOTE:
For accurate ORL measurement on instruments with two 2-way ports, insert a PC or APC Terminators as appropriate onto the unused ports to prevent stray light from entering the instrument.
*

## Slide 48: Instrument Operation ➥ Tone detection operation
Tone detection starts automatically when,
Instrument’s Meter port is connected to Source port of the same or a different instrument.
&
The output of the Source port is a standard test tone or Id tone.
  &
Instrument is at Home display (Main menu) or in Meter mode.
This feature is useful for quick continuity/polarity checking of fibers.
To stop tone detection:
Turn off Test/Id Tone mode of the Source (refer to Slide 36).
or
Turn on Slow Mode (refer to next slide).
Upon detecting a tone:
- for standard test/Id tone: the frequency and/or Id is displayed here.
- for non-standard tone: the actual measured frequency in Hz is displayed here (150 ~ 9999 Hz.)
- Instrument beeps to signify continuity.
Test or Id tone from another instrument
➟
Return to TOC
Single Instrument
A pair of Instruments
Upon detecting a tone:
- the frequency and/or Id is displayed here.
- Instrument beeps to signify continuity.
Loopback

## Slide 49: Instrument Operation ➥ Slow Mode operation
➀ Enter Slow Mode:
press F4 to go into Slow Mode.
In Slow Mode:
Beeping stops.
Display show average optical power of the modulated signal, using a long average.
➂ To exit Slow Mode:
Press F3 and F4 simultaneously to return to Tone Detection mode.
Flashing symbol indicating Slow Mode is activated.
Test or Id tone from source port of the same (loopback) or another instrument.
➟
Return to TOC
The average power (dBm) of detected tone.
Press F3 to change to display tone power in nW.
➟
➁ To enter Meter menu:
Press F3
Selected wavelength,. Press + or – to select other active wavelengths.
For single-unit operation (loopback):
When in Tone Detection mode, press F1 to go to this display.
➟

## Slide 50: Instrument Operation ➥ Memory operation ➥ Store data into internal memory
When instrument is operating in Meter or Autotest mode, press triangular button above “STORE” to save current measurement data in internal memory.
Note:
When data is being stored, the displays shows “bUSY” and will not respond to any keypress.
Once button is released, display will return to the last operation mode.
OR
Meter mode
Autotest mode
E.g., Data in Meter mode is saved along with the Text ID Tag, “TSST-A0001” in memory location ‘8’.
The memory location-pointer and the Text ID Tag are incremented after each save operation. In this example, the next data will be saved along with Text ID Tag “TSST-A0002” in location ’9’ .
Internal memory capacity:
8,000 fibers for one-way loss tests
4,000 fibers for two-way loss tests
Return to TOC
Text ID Tag

## Slide 51: Instrument Operation ➥ Memory operation ➥ Recall stored data from internal memory
At Home display (Main menu), press button above “MEMORY” to enter Memory mode.
Press – or + to select the memory location to display data.
Location ‘1’ has been selected in this example.
The content of the last memory location stored with data will be recalled and displayed i.e., location ‘6’ in this example.
Continue next page for viewing options for data saved in Meter mode.
Alternately displaying memory location & the Text ID Tag (if any) associated with the data.
Return to TOC

## Slide 52: Instrument Operation ➥ Memory operation ➥ Recall stored data from internal memory (continue)
Viewing options for data saved in Meter mode:
Press F3 to toggle display to show absolute power in watt only or, in both dBm and watt.
Absolute power in dBm
Absolute power in µW
Continue next page for viewing options for data saved in 1-way Autotest mode.
Return to TOC
Loss in dB
Reference power in dBm
Wavelength in nm
Absolute power in dBm

## Slide 53: Instrument Operation ➥ Memory operation ➥ Recall stored data from internal memory (continue)
Viewing options for data saved in 1-way Autotest mode:
Press F3 to toggle display to show absolute power in watt only or, in both dBm and watt.
Absolute power in ‘dBm’.
Absolute power displayed in both ‘dBm’ & ‘watt’.
Continue next page for viewing options for data saved in 2-way Autotest mode.
Return to TOC

## Slide 54: Instrument Operation ➥ Memory operation ➥ Recall stored data from internal memory (continue)
Viewing options for data saved in 2-way Autotest mode:
Press F3 to toggle display to show between,
- Test summary (showing loss of each direction & their average by wavelength)
- Test detail (showing absolute power, loss, reference power for each direction by wavelength)
- ORL values (only for instrument models built with this option)
Loss value (dB) measured on remote unit @ 1310 nm
Loss value (dB) measured on local unit @ 1310 nm
Average loss (dB) @ 1310 nm
Press F4 continuously to show data of all active wavelengths.
Absolute power (dB) measured on local unit @ 1310 nm
Loss (dB) value measured on local unit @ 1310 nm
Reference power (dB) of local unit @ 1310 nm
Test direction: remote-to-local
Test direction & data for local-to-remote unit.
Data @ 1550 nm
Test Summary Display
Test Detail Display
Test Detail Display
Return to TOC
If ORL option is available, press F3 to view relevant data.
Measured cable length (Km)
Symbol signifying loss test results (refer to Slide 16)
Symbol signifying loss test results (refer to Slide 17)

## Slide 55: Instrument Operation ➥ Memory operation ➥ Recall stored data from internal memory (continue)
Viewing options for data saved in 2-way Autotest mode: ORL data
ORL value (dB) measured on local unit @ 1550 nm
ORL value (dB) measured on remote unit @ 1550 nm
UCAL offset values for 1550 nm set on local unit (refer to slides 77, 78)
2-way Autotest ORL data display
Return to TOC
Symbol signifying ORL test result for a wavelength:
“✓” - Pass/fail check is disabled (threshold is set at “0.00”)
or
“✓” (pass) – passed ORL test
“X” (fail) – failed ORL test fails.
UCAL offset values for 1550 nm set on remote unit (refer to slides 77, 78)
Continue from last slide

## Slide 56: Instrument Operation ➥ Memory operation ➥ Recall stored data from internal memory (continue)
Viewing ORL data saved in manual ORL mode:
ORL value (dB) measured @ 1550 nm
Manual ORL data display
Return to TOC
UCAL offset values for 1550 nm set (refer to slides 77, 78)

## Slide 57: Instrument Operation ➥ Memory operation ➥ Recall stored data from internal memory (continue)
Viewing time stamp of saved data:
While viewing data saved in any of the 3 modes (Meter, 1-way Autotest, 2-way Autotest), hold down Toggle Centre.
Data saved in Meter mode
Data saved in 1-way Autotest mode
Data saved in 2-way Autotest mode
HOLD
OR
OR
HOLD
HOLD
HOLD
Release Toggle Centre now will return to the previous memory viewing display.
Continue next page for viewing nominal source power.
Return to TOC

## Slide 58: Instrument Operation ➥ Memory operation ➥ Recall stored data from internal memory (continue)
Viewing nominal source power:
While viewing data saved in 1-way Autotest or 2-way Autotest, hold down the left most rectangular button (above LCD).
Data saved in 1-way Autotest mode
Data saved in 2-way Autotest mode
To Exit Memory mode:
Press F1 and return to Home display (Main menu).
HOLD
Press F3 to show result in Test Detail Display.
HOLD
HOLD
HOLD
Return to TOC
Test Summary Display
Test Detail Display

## Slide 59: Instrument Operation ➥ Memory operation ➥ Retest or overwrite results
➁ Note currently displayed memory location:
E.g., the current location is ‘6’ is to be noted.
➂ Select memory location to overwrite data:
Press ‘–’ to go the location, then hold down button above “MEMORY” and press F2 for three seconds or until it stops beeping.
➀ Enter Memory mode:
At Home display (Main menu), press button above “MEMORY” to enter memory mode.
HOLD
E.g., Memory location ‘3’ has been selected for retest (data overwriting).
Continue next page
➊ Note current memory location
➋ Go to memory location to retest (overwrite data)
Return to TOC

## Slide 60: Instrument Operation ➥ Memory operation ➥ Retest or overwrite results (continue)
➄ Perform retest:
E.g., enter Meter (press F3) or Autotest (press F4) as needed.
➅ Save retest data:
Press triangular button above “STORE”.
This retest data will overwrite the saved data in location ’3’ selected in step ➂
➃ Exit memory mode:
Press F1.
Continue next page
➌ Retest and save (overwrite) data
E.g., Retest is performed in Autotest mode (F4 was pressed).
Return to TOC

## Slide 61: Instrument Operation ➥ Memory operation ➥ Retest or overwrite results (continue)
➇ Enter Memory mode:
Press button above “MEMORY”.
➆ End retest:
E.g. end Autotest by pressing F1.
➍ Return memory location pointer for next storage to where it was before retest
➈ Set memory location pointer for next storage:
Press ‘+’ to select location pointer ‘7’ in this example, as location ‘6’ was “noted” in step ➁.
Then, hold down button above “MEMORY” and press F2 for three seconds or until it stops beeping.
Next store operation will save data into location ‘7’.
Press F1 now will exit Memory mode and return to Home Display(Main menu).
HOLD
Return to TOC

## Slide 62: Instrument Operation ➥ Memory operation ➥ Transfer internally stored data onto USB stick
➀ At Home display (Main menu), insert USB stick onto instrument’s connector marked “MEM”.
➂ Press Triangle-button to start data transfer.
Data transfer is completed when instrument stops beeping and/or USB stick stops flashing.
Press F1 to power down USB stick before unplugging it from instrument.
➁ Press button above “MEMORY” to enter memory mode and, power up USB stick.
“USB” will be displayed. You may need to wait for a few second for USB to fully initialize before moving on to the next step.
Return to TOC

## Slide 63: Instrument Operation ➥ Memory operation ➥ Clear internal memory
➀ At Home display (Main menu), press button above “MEMORY” to enter memory mode.
➁ Hold down button above “MEMORY” then, press and hold F2 followed by F4 until “Clr” is displayed.
When unit stops beeping, content saved in all memory locations is erased.
HOLD
HOLD
HOLD
Press F1 now will exit Memory mode and return to Home Display(Main menu).
Return to TOC

## Slide 64: Instrument Operations ➥ Instrument Data Sanitization
This will erase all data in memory, reset all pass/fail thresholds to “0”, reset all reference values to “0”, reset Text ID Tag to “TEXT-A0001” , reset ORL UCAL & NF (for Zero Function) to factory defaults.
➀ Switch on instrument:
Press green button.
➁ Enter Memory mode:
Press button above ‘MEMORY’.
➂ Press and hold [MEMORY] & F2 simultaneously then, quickly press and hold F4 & Toggle Centre simultaneously for 3 seconds until beeping stops.
Sanitization in progress.
Note: Previously set date/ time & saved Text ID Tag will not be erased.
HOLD
HOLD
HOLD
HOLD
Return to TOC
Instrument will turn off

## Slide 65: Instrument Operation ➥ Text ID Tag operation
➌ Select new alphanumeric character, press ‘+’or ‘-’.
“AAAAAA001” is displayed with its 1’st character highlighted (flashing) for modification.
A useful auto-naming feature to systematically pre-configure (project) text names for test results stored in memory.
➀ Create a New Text ID Tag:
➊ In Meter or Autotest mode, press button above “FIBERID”.
➋ Enter Text ID Tag creation mode, press F4.
Flashing “- - - - - -0001” If no Text ID Tag has previously been created & stored.
Continue next page
Possible characters selectable for Text ID Tag:
First 6 digits: “blank”, “-”, “A~B”, “0~9”
Last 4 digits (for fiber indexing): ” 0~9”.
Return to TOC

## Slide 66: Instrument Operation ➥ Text ID Tag operation (continue)
DEL
➀ Create a New Text ID Tag (continue):
➎ Store the newly created Text ID, press F2.
Press F1 will quit without saving.
Up to 20 user-created Text ID Tags can be stored.
Newly created and stored Text ID Tag.
➍ Move on to enter the next character, press Toggle Centre.
Return to TOC

## Slide 67: Instrument Operation ➥ Text ID Tag operation (continue)
➁ To use a Text ID Tag:
➊ In Meter or Autotest mode, press button above “FIBERID”.
➋ Select a stored Text ID Tag, press ‘+’or ‘-’.
➌ Confirm selection, press F2.
Selected Text ID Tag for use.
Note:
During the next data storing operation, this will be saved along with data into internal memory.
The last 4 fiber indexing digits of the tag will increment after each memory store operation.
E.g.,“TEST-A0001” has been selected
Return to TOC

## Slide 68: Instrument Operation ➥ Text ID Tag operation (continue)
DEL
➂ To modify a Text ID Tag:
➊ In Meter or Autotest mode, press button above “FIBERID”.
➋ Select the Text ID Tag for modification, press ‘+’or ‘-’.
➌ Enter edit mode, press F3.
E.g., “TEST-E2101” is selected.
➍ Move to the character/s to modify, press Toggle Centre.
Continue next page
Return to TOC

## Slide 69: Instrument Operation ➥ Text ID Tag operation (continue)
DEL
DEL
➂ To modify a Text ID Tag (continue):
➎ Modify selected character, press ‘+’or ‘-’.
➏ Reset the Fiber Indexing digits to “0001”, press F3.
➐ Save modification, press F2.
Press F1 will quit without saving.
E.g., Text ID Tag has been modified to “TEST-H0001” .
E.g., Character “E” is selected for modification.
DEL
E.g., The selected “E” has been changed to “H”.
The last 4 digits are reset to ”0001”.
Return to TOC

## Slide 70: Instrument Operation ➥ Text ID Tag operation (continue)
➃ To delete a stored Text ID Tag:
➊ In Meter or Autotest mode, press button above “FIBERID”.
➋ Select a stored Text ID Tag to delete, press ‘+’or ‘-’.
➌ Enter edit mode, press F3
E.g.,“TEST-H0001” has been selected for deletion.
➍ Delete the selected Text ID Tag, press F4
➎ Confirm deletion, press F2.
Return to TOC

## Slide 71: Instrument Operation ➥ Visible laser operation
➀ Enter Source mode:
At Home display, press F1.
➁ Select 650 nm:
Press ‘+’or ‘-’.
➂ Select blinking output mode:
Press F3 to select “2 Hz” tone.
➃ Return to CW output mode: hold down F3 for 3 seconds.
➄ Turn off Visible laser & exit Source mode: Press Toggle Centre then press F1.
HOLD
CW output is on
2 Hz blinking output of 650 nm
Selected 650 nm visible laser
Return to TOC

## Slide 72: Instrument Settings ➥ Date & time
➀ Enter date & time setting mode:
When instrument is off, hold Toggle Centre then press green button.
➁ Select item to change:
Press Toggle Centre to select item. Selected item will flash.
Items toggle in the sequence,
Hour > Minute > Month > Day > Year
➂ Change value of selected item:
Press – or + key.
➃ Save settings:
Press F2.
Press F1 [CANCELL] will return to Main menu without saving the new settings.
Return to TOC

## Slide 73: Instrument Settings ➥ To deactivate beeping
To reactivate beeping:
Switch instrument off and back on.
➀ When instrument is off, hold down F2 then press green button.
➁ Continue to hold down F2.
➂ Release F2.
Beeping-deactivated indicator
HOLD
HOLD
Return to TOC

## Slide 74: Instrument Settings ➥ To activate Slow Mode at instrument switch-on
To deactivate Slow Mode:
Switch instrument off and back on.
➀ When instrument is off, hold down F3 then press green button.
➁ Continue to hold down F3.
➂ Release F3.
Slow Mode-activated indicator (flashing)
HOLD
HOLD
Return to TOC

## Slide 75: Instrument Settings ➥ Pass / fail thresholds setting
HOLD
HOLD
….OR.…
Pass / fail thresholds (for loss, optional cable length, optional ORL) can be set directly on instrument or downloaded from KITS software.
Note:
Auto Pass/fail checks for loss only works for 1-way or 2-way Autotest.
Auto pass/fail checks for length and ORL only works for 2-way Autotest.
For accurate auto pass/fail result on instrument models without ORL & cable Length measurement options, set all the corresponding threshold values to “0”.
To download the thresholds from KITS, refer to KITS software manual (coming soon!).
To setup the thresholds directly on instrument, refer to the instructions on this and the following pages.
➀ Enter pass/fail setting mode:
When instrument is off,
[For SM @ left 2-way port]: Hold down “–” and then press green button.
[For MM @ right 2-way port]: Hold down “+” and then press green button
Note: Only release “–” or “+” when threshold setting display shows up.
Continue next page
“IMPORTED” will show if a threshold setting has been imported from KITS and, change to “SETUP” if any changes are made locally.
Return to TOC
SM port
MM port

## Slide 76: Instrument Settings ➥ Pass / fail thresholds setting (continue)
➂ Edit value of selected item:
Press – or + to change values of selected item.
Note:
For accurate auto pass/fail result, the set values (magnitude) for MARGINAL must always be greater than that for PASS.
If value of a selected item is set at 0, auto pass/fail check for that item is disabled.
➃ Select pass / fail method:
Toggle F4 to select between AV (Average method) or WC (Worst Case method).
Note: Worst Case method always apply for 1-way Autotest regardless of whether AV or CW has been selected.
Continue next page…..
to set ORL thresholds (if this option is available)
to save settings
➁ Select item:
Press Toggle Centre to select item (among PASS, MARGINAL, length). Selected item will flash.
WC or AV mode
Return to TOC
For loss & optional cable-length:
SETUP
SETUP

## Slide 77: Instrument Settings ➥ Pass / fail thresholds setting (continue)
➅ Select item:
Press Toggle Centre to highlight value of item to be edited.
➆ Edit value of selected item:
Press – or + to change values of selected item.
Note: if value of selected item is set at 0, pass / fail check for ORL for that item is disabled.
➇ Save settings:
Press F2 (screen will return to Home Display).
Or press F1 will exit to Home Display without saving the new settings.
➄ Enter ORL thresholds setting display :
Press F3
Return to TOC
For optional ORL:
Loss thresholds setting Display
ORL thresholds setting Display
SETUP

## Slide 78: Instrument Settings ➥ ORL UCAL (User CALibration) setting
➃ Enter UCAL setting mode:
Press F3.
➀ Enter ORL (RETURN LOSS) measurement mode:
At Home Display, press F2.
Return to TOC
This sets up the instrument with an optical reference condition to compensate for optical loss in a test jig.
Unused 2-way port inserted with terminator
➁ Select wavelength for setting:
Press – or +
1310 nm has been selected in this example.
Continue next page
➂ Connect test jig (or launch cord etc.) to the 2-way port.
Read & note ORL reading on display, -12.3 dB in this example.

## Slide 79: Instrument Settings ➥ ORL UCAL (User CALibration) setting……continue
➄ Enter/edit value of UCAL offset:
Press – or + to enter the required offset (possible range:-9.99~9.99) on instrument.
In this example, UCAL offset of -2 dB is required, as ORL of test jig is measured at -12.3 dB when compared to the expected -14.3 dB of a known good reference SMF test cord.
Entered UCAL offset (dB)
Return to TOC
Resultant ORL value of DUT with UCAL offset factored in.
Note:
UCAL offset for different wavelengths need to be set individually.
The saved UCAL offsets are used for ORL measurements during 2-way Autotest or manual ORL measurement mode.
The UCAL offsets are only effective on measurements made by the instrument on which these offsets are saved.
➅ Save settings:
Press F2 to save and return to ORL measurement mode.
Or press F1 to return to ORL measurement mode without saving.
➆ Connect DUT to the test jig (or launch cord etc.).
Test jig + DUT
➇ To exit ORL measurement mode: Press F1 to return to Home Display.

## Slide 80: Instrument Settings ➥ ORL Zero Function
Return to TOC
This compensates for stray (residual) reflections to allow testing of weak reflection levels. Using this feature, the instrument can read accurately up to 10 dB below the stray reflection level. However, this feature causes increased noise, so when using this feature, ORL test resolution is decreased.
This setting is default at -65 dBm. For instrument with Ge meter detector, “ lo” will be the displayed value.
➁ Enter Zero Function setting mode:
Press F3 twice.
➀ Enter ORL (RETURN LOSS) measurement mode:
At Home Display, press F2.
Unused 2-way port inserted with terminator
➂ Determine Noise Floor (NF) of DUT:
Connect DUT to the 2-way port, connect far end of DUT with an appropriate Terminator.
Terminator
DUT
Continue next page
➃ Set NF of the instrument:
Press and hold F2 until it stops beeping.
Note:
This will automatically set and save NF of all active wavelengths on instrument.
Default NF value (-65 dBm or “Lo” on instrument with Ge meter detector
“NT” indicates in Zero Function setting mode

## Slide 81: Instrument Settings ➥ ORL Zero Function (continue)
➄ Measure actual ORL of DUT:
Removed Terminator from DUT and read DUT’s ORL from display.
With Terminator removed
DUT
Display will returns to ORL measurement mode with, new NF values automatically saved for all wavelengths.
DUT
ORL value of DUT
➅ To exit ORL measurement mode: Press F1 to return to Home Display.
Return to TOC

## Slide 82: Instrument Settings ➥ Reset ORL UCAL & NF (for Zero Function) to factory defaults
➀ Enter ORL (RETURN LOSS) measurement mode:
At Home Display, press F2.
➁ Enter Zero Function setting mode:
Press F3 twice (select EDIT followed by MODE).
➂ Reset NF & UCAL to default values (NF=65.00 dB, UCAL offset=0.00 dB):
For instrument model with a single 2-way port (SM or MM):
For MM port- Hold down F2 followed by “+” until it stops beeping.
or
or
For instrument model with two 2-way ports (SM & MM):
Home Display
ORL mode Display
ORL mode Display
Zero Function setting Display
Zero Function setting Display
Zero Function setting Display
SM
port
MM
port
Return to TOC
For SM port- Hold down F2 followed by “-” until it stops beeping.
X 2
Hold down F2 followed by Toggle Centre until it stops beeping.

## Slide 83
Keep the instrument in a carry case during storage and transport
Use only high-quality batteries.
For prolonged storage remove batteries.
The instrument is resistant to normal dust and moisture however, it is not waterproof.
  If moisture gets into the instrument, remove batteries & dry it out carefully before using it again.
Where possible, keep instrument away from strong sunlight.
Clean the instrument case using Isopropyl-alcohol (IPA) or other non solvent cleaning agents.
DO NOT use Acetone or other active solvents.
10 Instrument Care
Return to TOC

## Slide 84
Application Notes Comprehensive selection available at https://kingfisherfiber.com/application-notes/
Return to TOC

## Slide 85: Questions and Comments

## Slide 86: Thank you for your attention

## Slide 87
Revision record: |  |  | 
Revision | Date | Editor | Change descriptions
8 | 14Oct2024 | TO Ng | Added USB-C as USB connection or newer instrument version. Overall refinement.